## Slide 1: VISION 3.0 Smart Lock Manager APK Architecture, Design and Implementation
MARCH 2021
Dongsheng Zhang
Chaosheng Xiang
High confidential for NXP Solutions Internal ONLY!

## Slide 2: Introduction
High Level Functions:
  Feature Based Remote registration:
    Do the face data extraction on the mobile phone APK by oasis lite library with phone’s camera
    Send the extracted face feature with BLE to vision 3 KIT by BLE
    Do the face feature based registration in the vision 3 KIT
  Device Management
    Password based authentication
    Password update
  User management
    User list preview
    User name update
    User delete
Hardware Requirements:
  QN9090 BLE module connected to vision 3 KIT through the UART
  WUART profile in QN9090
  Remote Command
    Registration Command
    Deregistration Command
    Preview camera switch Command

## Slide 3: KEY Differences WITH vision 2
APK Side:
  Background
    QN9090 test APK “IoT Box” has the BLE WUART profile implementation(Whole BLE scan/pair/bound/WUART low level communication) which is matched with QN9090 WURAT firmware
    Vision 2 FaceRegManage APK has the Camera and Oasis Lite JNI implementation
    Add the Device management and User management, remote command for the vision 3 APK
  Strategy
    Leverage the BLE WUART part in “IoT Box” and the Camera and Oasis Lite JNI part in “FaceRegManager” to build our vision 3 Smart Lock Manager APK
    Use the raw data format transmission to reduce the transmission traffic and also the workload to parse/pack the transmission packet at the APK and device side
    Add the response for each packet request
VIZN3 Firmware Side:
  Redesigned low level UART transmission and remote event handling in vision 3 new framework design
  Updated registration flow:
    Design the new API in the oasis lite library to handle the registration with the face feature to align the registration flow with local registration(avoid the duplicate registration in the database)
    Use the RAW buffer instead of the JSON for the transmission to improve the performance and the memory/workload to parse the raw data from jason

## Slide 4: High level architecture --- APK side
Android Framework
Camera Device
BluetoothAdatper
BluetoothGattService
Bluetooth Device
BluetoothGattCharacteristic
CameraManager
CameraDevice
CameraCaptureSession
CaptureRequest
Surface
Algorithm Service
JNI
OASIS LITE Native library
BLE Device
Device Scan
Activity
Device
Authentication
Activity
Remote
Registration
Activity
Device
Manager
Activity
User
Manager
Activity
CPU
RAM
GPU
APK
UI
Camera Service
Algorithm Service
BLE Service
Packet Transmission Protocol

## Slide 5: High level architecture --- Device side
Camera Device
QN9090
M7
UART
FLASH
SLN Framework
Camera Manager
Display Manager
Input Manager
Output Manager
Algorithm Manager
SLN HAL
Camera Device
Display Device
UI Device
Oasis lite algorithm Device
Configuration Device
RT117F BSP
UART Driver
UART Packet Transmission
Packet Transmission Protocol
QN9090 Input Device Output Device
Smart Lock Firmware

## Slide 6: APK AND DEVICE COMMUNICATION process
Android Phone
Vision3 KIT
Connect
Authenticate
Scan
Transmit
Disconnect
Smart Lock Manager APK
Smart Lock Firmware

## Slide 7
Transmission Protocol:
  All the packet transfer are in raw data format
  Each packet transfer will be assembled with header transfer unit with fixed length and the data transfer unit with variable length
BLE WUART TRANSMISSION
APK
VIZN3
Header (fixed length)
Data (variable length)
Header (fixed length)
Data (variable length)
Request Packet
Response Packet
header transfer unit
data transfer unit
1 byte
1 byte
2 bytes
4 bytes
4 bytes
4 bytes
Transfer Unit Definition:
packet data
tu_type
pkt_type
pkt_len
pkt_id
pkt_crc
tu_crc

## Slide 8: Packet DEFINITION --- TRANSFER UNIT TYPE AND Packet type
TU Type | Value | Comment
header | 0x79 | Header TU
data | 0x80 | Data TU
Packet Type | Value | Comment | Direction
AUTHENTICATION_REQ | 0 | Authentication request | APK->Device
AUTHENTICATION_RES | 1 | Authentication response | Device->APK
UPDATE_PASSWORD_REQ | 2 | Update password request | APK->Device
UPDATE_PASSWORD_RES | 3 | Update password response | Device->APK
REGISTRATION_REQ | 4 | Remote registration request | APK->Device
REGISTRATION_RES | 5 | Remote registration response | Device->APK
DELETE_USER_REQ | 6 | Remote delete user request | APK->Device
DELETE_USER_RES | 7 | Remote delete user response | Device->APK
GET_USER_COUNT_REQ | 8 | Get user count request | APK->Device
GET_USER_COUNT_RES | 9 | Get user count response | Device->APK
GET_USER_INFO_REQ | 10 | Get user information request | APK->Device
GET_USER_INFO_RES | 11 | Get user information response | Device->APK
UPDATE_USER_INFO_REQ | 12 | Update user information request | APK->Device
UPDATE_USER_INFO_RES | 13 | Update user information response | Device->APK
REGISTRATION_CMD_REQ | 14 | Registration command request | APK->Device
REGISTRATION_CMD_RES | 15 | Registration command response | Device->APK
DEREGISTRATION_CMD_REQ | 16 | Deregistration command request | APK->Device
DEREGISTRATION_CMD_RES | 17 | Deregistration command response | Device->APK
PREVIEWCAMERA_SWITCH_CMD_REQ | 18 | Preview camera switch request | APK->Device
PREVIEWCAMERA_SWITCH_CMD_RES | 19 | Preview camera switch response | Device->APK

## Slide 9: Packet DEFINITION --- AUTHENTICATION
AUTHENTICATION_REQ |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 0
 | pkt_len | 2 | 6
 | pkt_id | 4 | ID of this packet
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | password | 6 | Password user typed in
AUTHENTICATION_RES |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 1
 | pkt_len | 2 | 1
 | pkt_id | 4 | same ID in the REQ
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | Authentication status | 1 | 0: success other: error code

## Slide 10: Packet DEFINITION --- UPDATEPASSWORD
UPDATEPASSWORD_REQ |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 2
 | pkt_len | 2 | 6
 | pkt_id | 4 | ID of this packet
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | password | 6 | New password
UPDATEPASSWORD_RES |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 3
 | pkt_len | 2 | 1
 | pkt_id | 4 | same ID in the REQ
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | Password update status | 1 | 0: success other: error code

## Slide 11: Packet DEFINITION --- REGISTRATION
REGISTRATION_REQ |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 4
 | pkt_len | 2 | 432
 | pkt_id | 4 | ID of this packet
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | name | 32 | User name
 | Face data | 400 | Face data
REGISTRATION_RES |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 5
 | pkt_len | 2 | 1
 | pkt_id | 4 | same ID in the REQ
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | Registration status | 1 | 0: success 1: duplicate registration Other: error code

## Slide 12: Packet DEFINITION --- registration apk side:
Extract the
face data with oasis
lite
Collect the user name
GRAY88 frame
Registration
Result Feedback
Send Task
Low
level
BLE
uart
send
receive
Receive Task
Assembly the
Packet
Send Packet
Receive Packet
Parse Packet
Face
data
Face
Name
Camera
RGB frame

## Slide 13: Packet DEFINITION --- registration device side:
Input device:
ble uart
Output device:
ble uart
Input notify:
Remote registration
event
Valgo device:
oasis lite
Output device:
ui
Output device:
console
BLE task
Remote
registration
Packet
Remote
registration
Response
Packet
Valgo result update:
Remote registration
mode result
input_notity()
input_notity()
input_notity()
Remote registration
input_notity()
input_notity()
BLE UART
Algorithm
Outputs
Low
level
BLE
uart
send
receive

## Slide 14: Packet DEFINITION --- DELETE_USER
DELETE_USER_REQ |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 6
 | pkt_len | 2 | 4
 | pkt_id | 4 | ID of this packet
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | Face id | 4 | Unique face id
DELETE_USER_RES |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 7
 | pkt_len | 2 | 1
 | pkt_id | 4 | same ID in the REQ
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | Delete user status | 1 | 0: success Other: error code

## Slide 15: Packet DEFINITION --- GET_USER_COUNT
GET_USER_COUNT_REQ |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 8
 | pkt_len | 2 | 0
 | pkt_id | 4 | ID of this packet
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | None |  | 
GET_USER_COUNT_RES |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 9
 | pkt_len | 2 | 4
 | pkt_id | 4 | same ID in the REQ
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | User count | 4 | User count

## Slide 16: Packet DEFINITION --- GET_USER_INFO
GET_USER_INFO_REQ |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 10
 | pkt_len | 2 | 0
 | pkt_id | 4 | ID of this packet
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | None |  | 
GET_USER_INFO_RES |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 11
 | pkt_len | 2 | 36
 | pkt_id | 4 | same ID in the REQ
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | User ID | 4 | User ID
 | User Name | 32 | User name

## Slide 17: Packet DEFINITION --- update_USER_INFO
UPDATE_USER_INFO_REQ |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 12
 | pkt_len | 2 | 0
 | pkt_id | 4 | ID of this packet
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | User ID | 4 | The ID of the user to be updated
 | User Name | 32 | The new name to update
UPDATE_USER_INFO_RES |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 13
 | pkt_len | 2 | 36
 | pkt_id | 4 | same ID in the REQ
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | Update status | 1 | 0:success Other: error code

## Slide 18: Packet DEFINITION --- registration_cmd
REGISTRATION_CMD_REQ |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 14
 | pkt_len | 2 | 0
 | pkt_id | 4 | ID of this packet
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | None |  | 
REGISTRATION_CMD_RES |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 15
 | pkt_len | 2 | 1
 | pkt_id | 4 | same ID in the REQ
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | Send command status | 1 | 0: command send success Other: error code

## Slide 19: Packet DEFINITION --- deregistration_cmd
DEREGISTRATION_CMD_REQ |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 16
 | pkt_len | 2 | 0
 | pkt_id | 4 | ID of this packet
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | None |  | 
DEREGISTRATION_CMD_RES |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 17
 | pkt_len | 2 | 1
 | pkt_id | 4 | same ID in the REQ
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | Send command status | 1 | 0: command send success Other: error code

## Slide 20: Packet DEFINITION --- PREVIEWCAMERA_SWITCH_cmd
PREVIEWCAMER_SWITCH_CMD_REQ |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 18
 | pkt_len | 2 | 0
 | pkt_id | 4 | ID of this packet
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | None |  | 
PREVIEWCAMERA_SWITCH_CMD_RES |  |  | 
 | Items | Bytes | Value
Header TU | tu_type | 1 | 0x79
 | pkt_type | 1 | 19
 | pkt_len | 2 | 1
 | pkt_id | 4 | same ID in the REQ
 | pkt_crc | 4 | 
 | tu_crc | 4 | 
Data TU | Send command status | 1 | 0: command send success Other: error code

## Slide 21: APK ui flow
Smart Lock Manager
Scan
VIZN3
Scan
Smart Lock Manager
Connected
Authenti
cation
VIZN3
Change Password
Registra
tion
User
Manger
Smart Lock Manager
Registration
Start
Smart Lock Manager
Reg Confirm
Name:
Smart Lock Manager
…
0 : Dongsheng Zhang
User Manager
1 : Chaosheng Xiang
…
Name:
ID:
0
Name:
ID:
1
Chaosheng Xiang
Delete
Update
Password:
Authentication
New:
Cancel
Change Password
Old:
Ok
Cancel
Ok
Cancel
Ok
Chaosheng Xiang
Cancel
Ok
Cancel
Ok
Remote
Command
Smart Lock Manager
Registration
Remote Command
Preview Camera Switch
Deregistration
Connected
Connected
Connected
Sending/Finished/Failed